## Slide 1: BEng (Hons) Control and Automation
Automation and Robotics
CRN: 50295
Dr Saber Mahboubi
Email: s.mahboubiheydarabad@salford.ac.uk

## Slide 2: Lecture Content: Introduction to Control in Automation

## Slide 3: Industrial Automation
The technology by which a process or procedure is accomplished without human assistance.
A technique that can be used to reduce costs and/or to improve quality.
A process which increases manufacturing speed, while reducing cost.
Can lead to products having consistent quality, perhaps even consistently good quality
Is normally implemented using a program of instructions combined with a control system that executes the instructions.
Which….

## Slide 4: Quick History
Automation has gone through a number of stages
Manual Control

## Slide 5: Industrial Automation
Automation is a technology concerned with application of mechanical, electronic and computer-based system to operate and control system. This technology includes;
Automatic assembly machines
Automation machine tools to process parts
Industrial robots
Automatic materials handling and storage system
Automatic inspection system and quality control
Feedback control and computer process control
Computer systems for planning, data collection and decision making to support manufacturing activities

## Slide 6: Basic Elements of an Automated System
The Actuator
  The actuator does the work
    Controlled by the controller.
    The actuator in a automated process may in fact be several actuators, each of which provides an output that drives another in the series of actuator.
Some actuators can only be on and off. Other actuators respond proportionally with the signal they receive from a controller
Actuators are ultimately controlled by an electrical signal although this controls other force providing media such as.
Electromotive
Pneumatic
Hydraulic

## Slide 7: Basic Elements of an Automated System
The Controller
  Tells the actuator to do the work
A controlled system either may be a digital system or an analogue system
Digital and analogue controllers are available ‘off the shelf’ so that systems can be constructed inexpensively and with little specialized knowledge required.
Modern automated control is almost exclusively PLC based

## Slide 8: Basic Elements of an Automated System
The Sensors
  provides feedback to the controller so that it knows the actuator is doing the work
  Obviously, controlled automation requires devices to sense system output.
  Sensors also can be used so that a controller can detect and respond to changing conditions in its working environment
  Switches and transducers are another name for sensors.
    Switches can detect when a measured condition exceeds a pre-set level. Example: closes when a work-piece is close enough to work on.
    Transducers can describe a measured condition. Example: output increased as level in tank raises.

## Slide 9: Automation
Robots just one tool in automation
There are different types of automation and equipment used in it
Selection of the appropriate type depends mainly on product variability and production volume

## Slide 10: Automation
Fixed (hard) automation
  Specialised machines
  Low variety
  High volume processes
  Maximum efficiency
  High equipment cost but high volume lowers manufacturing cost

## Slide 11
Programmable automation
  Low production volume
  High product variety
  Adaptable to variations but long change over times
  Control of a 'program’
    E.g. CNC machine making low volume specialist parts
  Low volume but premium charged because of this
Automation

## Slide 12: Automation
Flexible automation
  Between fixed & programmable automation
  Mid Volumes
  Some product variation and quick change over times
  Also called flexible manufacturing systems (FMS)
  Can be 'programmed'
  Robots considered flexible automation

## Slide 13: Automated Machine
Examples
  Fixed Automation
    Coke putting lids on bottles
    The production of washer or screws
  Programmable Automation
    An F1 team producing an engine block
    Airbus machining wing spars
  Flexible Automation
    Ford making 10 versions of the Focus
    Ginsters making sandwiches

## Slide 14
Automation

## Slide 15: Manufacturing System Classification
  Relationship between manufacturing systems

## Slide 16: Large Control System Hierarchy
  Manufacturing plants can have an extensive hierachical control system
Group control
Unit control
Field
Sensors
& actuators
A
V
Supervisory
Primary plant technology
SCADA
Supervisory Control
And Data Acquisition
T

## Slide 17: Large Control System Hierarchy
  Buses and processors in industrial plants form this hierarchy
PLC nodes
(multi-processors)
fieldbus (30m..2 km)
Operator panel
Mimic board
plant (Werk, usine)
P
disk
processor pool
transducers
control
stations
plant network (500m .. 3 km) – includes control network
valve
thermo-couple
motor
Process pictures
Process Data Base
Logging
position
backplane bus
node bus
workstation bus
instrument bus
(mimic board)
sensor bus
directly coupled
input/
output
open network, WAN
station
P
P
C
I/O
MEM
I/O
P
P
C
P
MEM
BC
station
M
sensor bus (0,5.. 30 m)

## Slide 18: Large Control System Hierarchy
  ABB Industrial IT (redundant system)
3rd party
controllers,
servers etc
Serial or fieldbus
engineering
workplace
Field Bus
Firewall
Plant Network / Intranet
Field Bus
Plant Network (Ethernet)
3rd party application server
application
server
aspect
server
Workplaces
(clients)
Enterprise
Optimization
(clients)
Mobile Operator
connectivity
server
Control Network (Ethernet)
Programmable
Logic Controller
AC 800C
Redundant
AC 800M
touch-screen
sensor network

## Slide 19: Fundamentals of Control Systems
Definitions
System – An interconnection of elements and devices for a desired purpose.
Control System – An interconnection of components forming a system configuration that will provide a desired response.
Process – The device, plant, or system under control. The input and output relationship represents the cause-and-effect relationship of the process.
Process
Output
Input

## Slide 20: Fundamentals of Control Systems
Definitions
Controlled Variable– It is the quantity or condition that is measured and Controlled. Normally controlled variable is the output of the control system.
Manipulated Variable– It is the quantity of the condition that is varied by the controller so as to affect the value of controlled variable.
Control – Control means measuring the value of the controlled variable of the system and applying the manipulated variable to the system to correct or limit the deviation of the measured value from a desired value.

## Slide 21: Fundamentals of Control Systems
Definitions
Disturbances– A disturbance is a signal that tends to adversely affect the value of the system. It is an unwanted input of the system.
If a disturbance is generated within the system, it is called internal disturbance. While an external disturbance is generated outside the system.
Controller
Output
Or
Controlled Variable
Input
or
Set point
or
reference
Process
Manipulated Variable

## Slide 22: Fundamentals of Control Systems
If a human operator is available to monitor and control a manufacturing process, open loop control may be acceptable
If a manufacturing process is automated, then it requires closed loop control , also known as feedback control .

## Slide 23: Fundamentals of Control Systems
Open-Loop Control Systems utilize a controller or control actuator to obtain the desired response.
Output has no effect on the control action.
In other words output is neither measured nor fed back.
Controller
Output
Input
Process
Since in open loop control systems reference input is not compared with measured output, for each reference input there is fixed operating condition. Therefore, the accuracy of the system depends on calibration.
The performance of open loop system is severely affected by the presence of disturbances, or variation in operating/ environmental conditions.

## Slide 24: Fundamentals of Control Systems
Closed-Loop Control Systems utilizes feedback to compare the actual output to the desired output response.
Controller
Output
Input
Process
Comparator
Measurement

## Slide 25: Fundamentals of Control Systems
  Temperature control using a room heater
  Cruise control in a car

## Slide 26: Fundamentals of Control Systems
  Position control in a human limb
  Level control in a dam

## Slide 27: Feedback Systems
A generalised feedback system

## Slide 28: Feedback Systems
Adding Values to the Feedback System

## Slide 29: Feedback Systems
Thus
This the transfer function of the arrangement
Terminology:
    A is also known as the open-loop gain
    G is the overall or closed-loop gain

## Slide 30: Feedback Systems
Effects of the product AB
  If AB is negative
    If AB is negative and less than 1, (1 + AB) < 1
    In this situation G > A and we have positive feedback
  If AB is positive
    If AB is positive then (1 + AB) > 1
    In this situation G < A and we have negative feedback
    If AB is positive and AB >>1
    - gain is independent of the gain of the forward path A

## Slide 31: Feedback Systems
Negative feedback can be applied in many ways
  Xi and Xo could be temperatures, pressures, etc.
  But mainly occurs as voltages and currents
Important in overcoming variability
  all active devices suffer from variability
    their gain and other characteristics vary with temperature and between devices
  using negative feedback we can produce an arrangement where the gain is independent of the gain of the forward path
    this gives us a way of overcoming problems of variability

## Slide 32: Types of Control System
Linear Vs Nonlinear Control System
A Control System in which output varies linearly with the input is called a linear control system.
y(t)
u(t)
Process

## Slide 33: Types of Control System
Linear Vs Nonlinear Control System
When the input and output has nonlinear relationship the system is said to be nonlinear.

## Slide 34: Types of Control System
Time invariant vs Time variant
When the characteristics of the system do not depend upon time itself then the system is said to time invariant control system.
Time varying control system is a system in which one or more parameters vary with time.

## Slide 35: Types of Control System
Continuous Data Vs Discrete Data System
In continuous data control system all system variables are function of a continuous time t.
x(t)
t
X[n]
n
A discrete time control system involves one or more variables that are known only at discrete time intervals.

## Slide 36
Deterministic vs Stochastic Control System
If not, the control system is a stochastic control system
y(t)
t
x(t)
t
z(t)
t
Types of Control System
A control System is deterministic if the response to input is predictable and repeatable

## Slide 37: Types of Control System
Classification of Control Systems
LTI Control Systems(Linear time invariant control systems)

## Slide 38: Transfer Functions
Calculation of control transfer functions
x(t)
y(t)
Transfer functions may require the solution of first, second or even higher differential equations
To make this problem easier to solve we use Laplace Transforms
Laplace
transform
solution
in
s domain
inverse
Laplace
transform

## Slide 39: Transfer Functions
Laplace Transform Domain
Transfer functions may require the solution of first, second or even higher differential equations
linear
differential
equation
time
domain
solution
Laplace
transformed
equation
Laplace
solution
Time domain
algebra
Laplace transform
inverse Laplace
transform
Laplace domain or
complex frequency domain

## Slide 40: FOR TOMORROW
Have a look at the two YouTube videos
Laplace Transforms
https://www.youtube.com/watch?v=ZGPtPkTft8g
Transfer Functions
https://www.youtube.com/watch?v=RJleGwXorUk
Links available on blackboard