## Slide 1: BEng (Hons) Control and Automation
Automation and Robotics
CRN: 50295
Dr Saber Mahboubi
Email: s.mahboubiheydarabad@salford.ac.uk

## Slide 2: Lecture Content: Second Order Systems and PID controllers

## Slide 3: Introduction
We have already discussed the affect of location of the pole on the transient response of 1st order systems.
Compared to the simplicity of a first-order system, a second-order system exhibits a wide range of responses that must be analyzed and described.
Varying a first-order system's parameters (T, K) simply changes the speed and offset of the response
Whereas, changes in the parameters of a second-order system can change the form of the response.
A second-order system can display characteristics much like a first-order system or, depending on component values, display damped or pure oscillations for its transient response.

## Slide 4: Introduction
A general second-order system (without zeros) is characterized by the following transfer function.
Open-Loop Transfer Function
Closed-Loop Transfer Function

## Slide 5: Introduction
un-damped natural frequency of the second order system, which is the frequency of oscillation of the system without damping.
damping ratio of the second order system, which is a measure of the degree of resistance to change in the system output.

## Slide 6: Example
Determine the un-damped natural frequency and damping ratio of the following second order system.
Compare the numerator and denominator of the given transfer function with the general 2nd order transfer function.

## Slide 7: Introduction
The closed-loop poles of the system are

## Slide 8: Introduction
Depending upon the value of , a second-order system can be set into one of the four categories:
Overdamped - when the system has two real distinct poles ( >1).
-a
-b
-c
δ
jω

## Slide 9: Introduction
Depending upon the value of , a second-order system can be set into one of the four categories:
2. Underdamped - when the system has two complex conjugate poles (0 < <1)
-a
-b
-c
δ
jω

## Slide 10: Introduction
Depending upon the value of , a second-order system can be set into one of the four categories:
3. Critically damped - when the system has two real but equal poles ( = 1).
-a
-b
-c
δ
jω

## Slide 11: Introduction
Depending upon the value of , a second-order system can be set into one of the four categories:
4. Undamped - when the poles have no real component.
δ
jω

## Slide 12: Time-Domain Specification
Most systems are underdamped where 0< <1 and ωn > 0, these systems are of most interest. The 2nd order system’s response due to a unit step input looks like

## Slide 13: Time-Domain Specification
The delay (td) time is the time required for the response to reach half the final value the very first time.

## Slide 14: Time-Domain Specification
The rise time is the time required for the response to rise from 10% to 90%, 5% to 95%, or 0% to 100% of its final value.
For underdamped second order systems, the 0% to 100% rise time is normally used. For overdamped systems, the 10% to 90% rise time is commonly used.
14

## Slide 15: Time-Domain Specification
The peak time is the time required for the response to reach the first peak of the overshoot.
15
15

## Slide 16: Time-Domain Specification
The maximum overshoot is the maximum peak value of the response curve measured from unity. If the final steady-state value of the response differs from unity, then it is common to use the maximum percent overshoot. It is defined by
The amount of the maximum (percent) overshoot directly indicates the relative stability of the system.

## Slide 17: Time-Domain Specification
The settling time is the time required for the response curve to reach and stay within a range about the final value of size specified by absolute percentage of the final value (usually 2% or 5%).

## Slide 18: Using the S-Plane
δ
jω
Natural Undamped Frequency.
Distance from the origin of s-plane to pole is natural undamped frequency in rad/sec.

## Slide 19: Using the S-Plane
δ
jω
Let us draw a circle of radius 3 in s-plane.
3
-3
-3
3
If a pole is located anywhere on the circumference of the circle the natural undamped frequency would be 3 rad/sec.

## Slide 20: Using the S-Plane
δ
jω
Therefore the s-plane is divided into Constant Natural Undamped Frequency (ωn) Circles.

## Slide 21: Using the S-Plane
δ
jω
Damping ratio.
Cosine of the angle between vector connecting origin and pole and –ve real axis yields damping ratio.

## Slide 22: Using the S-Plane
δ
jω
For Underdamped system therefore,

## Slide 23: Using the S-Plane
δ
jω
For Undamped system therefore,

## Slide 24: Using the S-Plane
δ
jω
For overdamped and critically damped systems therefore,

## Slide 25: Using the S-Plane
δ
jω
Draw a vector connecting origin of s-plane and some point P.
P

## Slide 26: Using the S-Plane
δ
jω
Therefore, s-plane is divided into sections of constant damping ratio lines.

## Slide 27: Using the S-Plane

## Slide 28: Step Response of underdamped System

## Slide 29: Step Response of underdamped System

## Slide 30: Step Response of underdamped System

## Slide 31: Other Step Responses

## Slide 32: Step Responses by Pole Positions
Higher Frequency
Oscillation
Lower Frequency
Oscillation
No Oscillation
Increasing
Amplitude
Stable
Amplitude
Settling
Amplitude
Oscillations
Mirrored
(+/- Nature
of poles)

## Slide 33: Time Domain Specifications of Underdamped system
Time Domain Specifications (Settling Time)

## Slide 34: Time Domain Specifications (Settling Time)
Real Part
Imaginary Part

## Slide 35: Time Domain Specifications (Settling Time)
Settling time (2%) criterion
  Time consumed in exponential decay up to 98% of the input.
Settling time (5%) criterion
  Time consumed in exponential decay up to 95% of the input.

## Slide 36: Summary of Time Domain Specifications
Rise Time
Peak Time
Settling Time (2%)
Settling Time (5%)
Maximum Overshoot

## Slide 37: Example
Consider the system shown in following figure, where damping ratio is 0.6 and natural undamped frequency is 5 rad/sec. Obtain the rise time tr, peak time tp, maximum overshoot Mp, and settling time 2% and 5% criterion ts when the system is subjected to a unit-step input.

## Slide 38: Example
Rise Time

## Slide 39: Example
Peak Time
Settling Time (2%)
Settling Time (5%)

## Slide 40: Example
Maximum Overshoot

## Slide 41: PID Control

## Slide 42
The PID-controller is a “combination” of three different actions:
* The “P-Action”
* The “I-Action”
* The “D-Action”
PID-Control – Introduction
Industrial controllers come with different classifications
Proportional controllers
Integral controllers
Proportional-plus-integral controllers
Proportional-plus-derivative controllers
Proportional-plus-integral-plus-derivative controllers
This Lecture will explain these actions “one-by-one”, so that each action will be easy to understand

## Slide 43
The PID-controller combines the three actions in parallel
Proportional-Integral-Derivative (PID) Control
V
Y
At any given time the Error signal will be:

## Slide 44
Hence the transfer function of the controller is the sum of the three elements
Proportional-Integral-Derivative (PID) Control
The gain k can be weighted to determine the relative influence of each control type.

## Slide 45
Proportional-Integral-Derivative (PID) Control
 | Good | Bad
Proportional | Reduces steady-state error | Too much causes instability
Integral | Eliminates steady-state error | Too much causes instability
Derivative | Adds damping reduces overshoot | Amplifies noise

## Slide 46
Proportional Control
PB too big
C°
(t)
SV
gain correct
C°
(t)
SV
gain too small
C°
(t)
SV
A Proportional gain that is too high causes hunting! The TC will than behave like an ON/OFF controller!
A correctly sized P gain results in an Overshoot, followed by an Undershoot and than Stabilization, with a small offset near the Set Point.
With a low gain the Setpoint temperature will never be reached!
This will create a large offset from the Set Point!
The right setting of the proportional gain is very important

## Slide 47: Integral Control of Systems.
Integral control of the system eliminates the steady-state error in the response to the step input..

## Slide 48: Derivative Control
Derivative control introduces a damping effect. A typical response curve c ( t ) to a unit step input is shown

## Slide 49
Simulink Simulation of PID control system

## Slide 51
Over 60 years ago, Ziegler and Nichols (1942) published a classic paper that introduced the continuous cycling method for controller tuning. It is based on the following trial-and-error procedure:
The open loop step response curve of the process is recorded and the steepest tangent to the reaction curve is
drawn
PID controller tuning- Ziegler-Nichols reaction curve method

## Slide 52
The reaction curve is characterized by two parameters:
- Ƭ intercept of the steepest tangent with the time axis
- a modulus of the intercept of the steepest tangent with the time axis.
Note that Ƭ is an approximation of the time delay of the system and Ƭ/a is the steepest slope of the step response.
PID controller tuning- Ziegler-Nichols reaction curve method

## Slide 53
Table shows the PID tuning rules based on the two reaction curve parameters. The table also shows an estimate of the period of oscillation Tp of underdamped step response the closed loop system.
PID controller tuning- Ziegler-Nichols reaction curve method

## Slide 54
Also known as the Ziegler-Nichols frequency response (ZNFR) method.
With the system under proportional-only control, a unit step input is applied to the closed-loop system and the proportional gain is increased until the response is a sustained oscillation
PID controller tuning- Ziegler-Nichols ultimate gain method

## Slide 55
An alternative way to obtain the sustained oscillation required for the Ziegler–Nichols ultimate gain tuning method is to connect the process in a feedback loop with a nonlinear element having a square wave relay function
PID controller tuning- Ziegler-Nichols ultimate gain method

## Slide 56
PID controller tuning- Ziegler-Nichols ultimate gain method

## Slide 57
Ziegler-Nichols Table of Settings
Control Type | KP | KI | KD
P | 0.50KU | — | —
PI | 0.45KU | 0.54KU/TU | —
PID | 0.60KU | 1.2KU/TU | 3KUTU/40

## Slide 58
Relay Auto Tuning

## Slide 59
With more capable processors the auto tuning process could consist of:
Trying a small impulse signal and calculating tuning parameters from the response .
Looking at historical process data to derive the tuning parameters.
Starting with the Z-N values and trying small changes to look for improvements.
Basing the parameter on an entirely mathematical model of the process.
Modern Auto Tuning