## Slide 1: BEng (Hons) Control and Automation
Automation and Robotics
CRN: 50295
Dr Saber Mahboubi
Email: s.mahboubiheydarabad@salford.ac.uk

## Slide 2: Lecture Content: Robot Manipulator Kinamatics

## Slide 3: Robot Anatomy
Recall the construction of our manipulator arms
The manipulator consists of joints and links
  Joints provide relative motion
  Links are rigid members between joints
  Various joint types: linear and rotary
  Each joint provides a “degree-of-freedom”
  Most robots possess five or six degrees-of-freedom
The manipulator normally consists of two sections:
  Body-and-arm – for positioning of objects in the robot's work volume
  Wrist assembly – for orientation of objects

## Slide 4: Robot Joints
The more common joints types used are:
For translational motion
  Linear joint
  Orthogonal joint
For rotary motion
  Rotational joint
  Twisting joint
  Revolving joint

## Slide 5: Degrees Of freedom
The ability of a joint to operate in one or more of the 3 translational axes or rotational orientation
The combination of these can give the overall manipulator multiple degrees of freedom
Complete flexibility require 6 DOF
More DOF leads to more complex control
More than 6 DOF is possible if the manipulator is build for redundency

## Slide 6: Body and Arm Configurations
There are also a number of body and arm configurations
These are normally used as they reduce the complexity of the joints and the control in industrial environments where the workspace can be defined
The five common body-and-arm configurations for industrial robots are:
  Polar coordinate body-and-arm assembly
  Cylindrical body-and-arm assembly
  Cartesian coordinate body-and-arm assembly
  Jointed-arm body-and-arm assembly
  Selective Compliance Assembly Robot Arm (SCARA)

## Slide 7: Polar coordinate body-and-arm assembly
Consists of a sliding arm actuated relative to the body, which can rotate about both a vertical axis and horizontal axis

## Slide 8: Cylindrical body-and-arm assembly
Consists of a vertical column, relative to which an arm assembly is moved up or downand the arm can be moved in or out relative to the column

## Slide 9: Cartesian coordinate body-and-arm assembly
Consists of three sliding joints, two of which are orthogonal, also known as the rectilinear robot

## Slide 10: Jointed-arm body-and-arm assembly
Based on sets of revolute joints in a similar way to a human arm so mostly involving angular movement

## Slide 11: Selective Compliance Assembly Robot Arm (SCARA)
Similar to jointed-arm robot except that vertical axes are used for shoulder and elbow joints to be compliant in horizontal direction for vertical insertion tasks

## Slide 12: Kinamatics
KINEMATICS - the analytical study of the geometry of motion of a robot arm
In order to control and programme a robot we must have knowledge of both it’s spatial arrangement and a means of reference to the environment
  This is done:
  with respect to a fixed reference co-ordinate system
  without regard to the forces or moments that cause the motion
In order to describe the position and orientation of a body in space, we will always attach a coordinate system, or frame, rigidly to the object. We then proceed to describe the position and orientation of this frame with respect to some reference coordinate system

## Slide 13: Kinamatics
Kinamatics is concerned with being able to determine the position and orientation of the end effector (tool) of a robot with respect to its co-ordinate system
This requires the need of representing positions and orientations
i.e. the location of the parts, tools, and of the mechanism itself
To define and manipulate mathematical quantities which represent position there are co-ordinate systems and conventions for representation

## Slide 14: Axes
Axes are defined according to the right hand rule of orientation
Use z as the thumb, x as the direction the hand is pointing and y will be in the direction you curl your fingers.

## Slide 15: Frames
All parts of the robot and items in work cell will have a reference frame
Getting the correct position and orientation requires translation between the frames
z
y
x
Right-handed
Co-ordinate frame
Goal Frame
x
Link Frame
x
Camera Frame
Tool
Frame
Base
Frame
x
x
x

## Slide 16: Co-ordinates
Co-ordinates are cartesian but normally represented as a vector
The 3 elemets of the vector are simply the 3 cartesian co-ordinates in an x-y-z system.

## Slide 17: Orientation
In a robot system with rotational degrees of freedom you need represent a point in the space and describe the orientation of a body in space
Here the co-ordinate frame has got a positional relation to the original frame using AP .
If the box is rotated in any way we need to describe that rotation with respect to its position.
This is done with a rotational matrix.

## Slide 18: Orientation
In effect the rotational possibilities are represented by 3 vectors which are represented in a 3x3 matrix
So we have:
A vector to represent position
A 3x3 matrix to represent orientation
In this case 1=x, 2=y, 3=z

## Slide 19: Rotational Transforms
There are three possible rotational transforms that can be represented by this matrix
Rotation about Z-axis.
Rotation about X-axis.
Rotation about Y-axis.
Each may be applied individually or together using the matrix

## Slide 20: Z-axis rotation
Rotating around the z-axis by an angle θ
An axis that’s pointing out of the paper is denoted by ʘ, and an axis that’s pointing into the paper is denoted by O
X

## Slide 21: X-axis rotation
Rotating around the X-axis by an angle θ
An axis that’s pointing out of the paper is denoted by ʘ, and an axis that’s pointing into the paper is denoted by O
X

## Slide 22: Y-axis rotation
Rotating around the Y-axis by an angle θ
An axis that’s pointing out of the paper is denoted by ʘ, and an axis that’s pointing into the paper is denoted by O
X

## Slide 23: Multi axis transformation
Transformations through angles in all axes (γ: x-axis), (β : y -axis), (α: z-axis) can be done by applting each transformation individualy or by pre-calculating the resulting matrix.
c and s are used as a shortform for the cosine and sine functions

## Slide 24
Z(i - 1)
X(i -1)
Y(i -1)
Z i
Y i
X i
( i - 1)
a(i - 1 )
a i
d i
 i
Each joint is assigned a coordinate frame
 : A rotation about the z-axis.
d : The distance on the z-axis.
a : The length of each common normal (Joint offset).
 : The angle between two successive z-axes (Joint twist)
The Denavit-Hartenberg Notation
The Danavit-Hartenberg Notation is a set of parameters that can be assigned to each joint pair that allows the use of a common transformation matrix .
Using the Denavit-Hartenberg notation, you need 4 parameters to describe how a frame (i) relates to a previous frame ( i -1 ).

## Slide 25
The joint axes are the axes around which revolution takes place which are the Z(i-1) and Z(i) axes.
The ‘a’ Parameter
  These two axes can be viewed as lines in space. The common perpendicular is the shortest line between the two axis-lines and is perpendicular to both axis-lines.
Z(i - 1)
X(i -1)
Y(i -1)
Z i
Y i
X i
( i - 1)
a(i - 1 )
a i
d i
 i
a(i-1) is the length of the perpendicular between the joint axes.
  If the link is prismatic, then a(i-1) is a variable, not a parameter

## Slide 26
Can also be the displacement along the Zi to align the X(i-1) and Xi axes.
The ‘d’ Parameter
Z(i - 1)
X(i -1)
Y(i -1)
Z i
Y i
X i
( i - 1)
a(i - 1 )
a i
d i
 i
The displacement along the Zi axis needed to align the a(i-1) common perpendicular to the ai common perpendicular.

## Slide 27
How much you have to rotate around the X(i-1) axis so that the Z(i-1) is pointing in the same direction as the Zi axis.
The ‘α’ Parameter
Z(i - 1)
X(i -1)
Y(i -1)
Z i
Y i
X i
( i - 1)
a(i - 1 )
a i
d i
 i
Amount of rotation around the common perpendicular so that the joint axes are parallel.

## Slide 28
The ‘ϴ’ Parameter
Z(i - 1)
X(i -1)
Y(i -1)
Z i
Y i
X i
( i - 1)
a(i - 1 )
a i
d i
 i
Amount of rotation around the Zi axis needed to align the X(i-1) axis with the Xi axis.

## Slide 29
Just like our earlier matrix, the Denavit-Hartenberg Matrix is a transformation matrix from one coordinate frame to the next.
Using a series of D-H Matrix multiplications and the D-H Parameter table, the final result is a transformation matrix from some final frame to your initial frame.
Z(i - 1)
X(i -1)
Y(i -1)
( i - 1)
a(i - 1 )
Z i
Y i
X i
a i
d i
 i
The Denavit-Hartenberg Matrix

## Slide 30
(I) Rotate about the zn-axis an able of n+1. (Coplanar)
(II) Translate along zn-axis a distance of dn+1 to make xn and xn+1
colinear.
(III) Translate along the xn-axis a distance of an+1 to bring the origins
of xn+1 together.
(IV) Rotate zn-axis about xn+1 axis an angle of n+1 to align zn-axis
with zn+1-axis.
The Denavit-Hartenberg Process
Note theY-axis is not used in D-H representation, so if the y-axis forms part of a robots physical movement capability the D-H method cannot be used.

## Slide 31: Position of End Effector
Hence it is possible to determine the position and orientation of the end effector in space with a manipulator having a full 6 degrees of freedom.
Each link requires a translational vector to describe the position of its end joint
Each joint requires a rotational matrix to describe the orientation of the next link
Chaining these together allows the position of the end effector to be found

## Slide 32: Forward Kinematics
Forward kinematics is the process by which you determine the position of the end effector given the link dimensions and joint angles.
To avoid extensive matrix calculations we will just use simpler trigonometric solutions for a planer robot (SCARA type)
Knowing the length of each link and its orientation allows the calculation of the position of the end joint
Chaining these together for each joint allows the position of the end effector to be found
b
(0,0)
a
Θ2
Θ1
Θ3
c

## Slide 33: Forward Kinematics
Dividing the problem up into successive right angled triangles allow us to do this.
This can be continued for any number of links
b
(0,0)
a
Θ2
Θ1
Θ3
c
Θ4
Θ5
x1
x2
x3
y1
y2
y3
x1=a cos θ1, y1=a sin θ1
θ4= θ2 – 90 – (180- θ1- 90)
x2=b cos θ4, y2=b sin θ4
θ5= θ3 – 90 – (180- θ4- 90)
x3=c cos θ5, y3=b sin θ5
Final co-ordinate: (x1 + x2 + x3, y1 + y2 + y3)

## Slide 34: Inverse Kinematics
Inverse kinematics is more useful ( and harder ) as the process by which you determine the joint angles based on the required co-ordinates of the end effector.
Again to avoid extensive matrix calculations we will just use simpler trigonometric solutions for a planer robot (SCARA type)
Knowing the length of each link allows us to work back from the end effector to construct a geometric solution
b
a
(x,y)
(0,0)
Θ2

## Slide 35: Inverse Kinematics
For this problem we need to construct linking triangles
L1
L2
(0,0)
(X,Y)
Θ1
Θ2
B
K2
K1
From this:
B2 = X2+Y2
K1=tan-1(Y/X)
(A=K2, b=L1, a = L2, c = B)
=
= (L12-L22+B2)/2L1B
K2=cos-1((L12-L22+B2)/2L1B)
Θ1= K1+ K2

## Slide 36: Inverse Kinematics
For this problem we need to construct linking triangles
This may need to be done for intermediate links for longer link chains
L1
L2
(0,0)
(X,Y)
Θ1
Θ2
B
K2
K1
(A=Θ2, b = L1, c = L2, a = B)
) /2L1 L2
Θ 2=cos-1((L12+L22-B2)/2L1 L2)

## Slide 37: Other Considerations
There are a few other things to account for when solving kinematic problems
Most joints will have restrictions which need to be accounted for in the controller
Most inverse kinematic solutions may have more than one solution
Calculation complexity rises as the number of degrees of freedom increase.
Use restricted DOF manipulator where possible to reduce control complexity

## Slide 38: Trajectory Planning
For a robot to operate efficiently it must be able to move from point to point in space.
A joint cannot instantly start moving at a constant velocity, there will be periods of acceleration and decceleration
So to provide an accurate position of any joint at any time the motion must be planned taking this into account
A trajectory is a time history of position, velocity and acceleration for each joint
This is known as the trajectory.
Trajectories are computed at run time and updated at a certain rate - the Path Update Rate

## Slide 39: Joint Space Trajectory Planning
Take this simple example
Consider a robot with only one link moving from A to B
Kinematics gives one configuration for B
There is a choice of two trajectories to get there
Sometimes a via point is required to force a trajectory or an algorithm for shortest route
B
(0 , t0)
f f
( , t )
A

## Slide 40: Joint Space Trajectory Planning
The trajectory from A to B as a function of time could be described by a number of functions
We can use the start and end constraints to construct a function for this
time
0
t
f
angle
f
Lots of choices for continuous functions
0

## Slide 41: Cubic Polynomials
There are 4 constraints we can consider
We know the starting angle at A, 0
B
(0 , t0)
f f
( , t )
A
We assume the starting velocity at A will be 0 , 0 = 0
.
We know the finishing angle at B, f
We assume the finishing velocity at B will be 0 , f = 0
.
(t )  a
0
a t  a t2  a t3
1 2 3
This requires a cubic polynomial with 4 coefficients to satisfy the 4 constraints

## Slide 42: Cubic Polynomials
We can differentiate the polynomial to get:
With our starting conditions we get a0=0 and a1= 0
(t ) 
a  2a t 3a t2
1 2 3
.
So:
and:
(tf ) 
2a t3a t2
2 3
.
 0
(tf )  
0
 a t2 a t3
2 3
= f

## Slide 43: Cubic Polynomials
From these simultaneous equations we get
a0  0
a1  0
t
f
2
2
f
3
a  (  0 )
t
f
3
3
f
2
a  
(  0 )
Now using the original formula and its derivative it would be possible to plot the angular and velocity profile as a function of time.
In situations with more constraints higher order polynomials can be used to provide a trajectory solution.

## Slide 44: Example
Lets try this with some actual numbers.
Angles will be in radians
Set the starting angle at A, 0, to -0.5rad
B
(0 , t0)
f f
( , t )
A
The starting velocity at A will be 0
.
Set the finishing angle at B, f, to 1.7rad
The finishing velocity at B must also be 0
.
Lets make the movement take place over 2s of time. (tf = 2)

## Slide 45: Example
First calculate the coefficients
a0  0
a1  0
t
f
2
2
f
3
a  (  0 )
t
f
3
3
f
2
a  
(  0 )
So:
a0  -0.5
a1  0
4
2
3
a  (2.2)=1.65
8
3
2
a  
(2.2)=0.55

## Slide 46: Example
Now we can put these into our two formula for angle at a given time and angular velocity at a given time:
and:
(t ) 
3.3 t -1.65 t2
.
(t )  -0.5
 1.65t2 -0.55 t3
By putting in values of t between 0 and 2 we can now plot the angle and velocity as a function of time.