## Slide 1: BEng (Hons) Control and Automation
Automation and Robotics
CRN: 50295
Dr Saber Mahboubi
Email: s.mahboubiheydarabad@salford.ac.uk

## Slide 2: Lecture Content: Robot Manipulator Dynamics

## Slide 3: Dynamics
Robot manipulator dynamics deals with the mathematical formulations of the equations of robot arm motion
They are useful as:
  An insight into the structure of the robot system
  A basis for model based control systems
  A basis for computer simulations
They are concerned with:
  Forces
  Moments
  Accelerations
  Velocities
  The effect of gravity
Forces, moments
Velocities, Accelerations
Gravity

## Slide 4: Robot Joints
Consider our joints again:
Use Force, linear acceleration, velocity for:
  Linear joint
  Orthogonal joint
Use Torque, angular acceleration,
angular velocity for:
  Rotational joint
  Twisting joint
  Revolving joint

## Slide 5: Equations of Linear Motion
Recall the basic Newtonian equations force and motion
F=ma
vf= vi+ at
d= vit + ½ at2
vf2 = vi2 + 2ad
  t is the time
  d is the displacement
  v is velocity
  a is the acceleration
  F is the force
  m is the mass
These formula can be applied at a basic level to any joint actuator combination that involves just linear motion

## Slide 6: Consideration of Forces
To use the equations of motion consideration needs to be given to forces acting on the joint
If we get the forces right a reasonable attempt can be at solving some problems
Actuator Force (F)
F→
Friction Force (FF)
←FF
Damping Force (FD)
←FD
Braking Force (FB)
←FB
Not forgetting gravity if our joint is acting at an angle
F→
←FF
←FD
←FB
FG→
θ
FG=mg cosθ
m is the mass of the bar, g is acceleration due to gravity

## Slide 7: Typical Dynamics Problem
You need your linear joint to move forward a distance d to connect the end effector with a part, it must not exceed the safe velocity v in transit.
Assume link is horizontal and we know the mass and forces involved
Actuator Force available (F)
Friction Force (FF)
Damping Force (FD)
Braking Force (FB)
F→
←FF
←FD
←FB
m
Divide the problem into 3 phases
Acceleration phase
(full actuator force)
Velocity(m/s)
Time (s)
v
Cruising phase
(actuator force counters
resistances)
Braking phase
(actuator off, brake on)

## Slide 8: Typical Dynamics Problem
Acceleration Phase.
Assume brake is off, so force available for acceleration is:
Fa = F - FF -FD
F→
←FF
←FD
←FB
m
So acceleration a is: a=Fa/m
Obtain ta from: vf= vi+ at
Obtain da from: d= vit + ½ at2
Braking Phase.
Assume brake is on, actuator is off so total braking force is:
Fb = FB + FF +FD
So deceleration -a is: a=Fb/m
Obtain tb from: vf= vi+ at
Obtain db from: d= vit + ½ at2

## Slide 9: Typical Dynamics Problem
Cruising Phase.
Assume actuator force set to balance resistive forces
Fc = 0
We know the travel distance required is d and we know the distance travelled in the other two phases. So the distance required in the cruising phase is:
dc =d -da -db
So the joint needs to spend ta with the actuator full on and no brake
tc with the actuator countering resistive forces and
tb with the brake full on and no actuator
At which point it should reach its destination d at a full stop
So the time in the cruising phase must be tc= dc /v

## Slide 10: Equations of Angular Motion
Also recall the basic Newtonian equations angular force and motion which are direct equivalents to the linear equations of motion
  t is the time
  θ is the displaced angle
  ω is angular velocity
  α is the angular acceleration
The big difference with angular dynamics is the force based equation which uses torque (τ) and a quantity known as the moment of inertia (I)
τ=Iα

## Slide 11: Moment of Inertia
Moment of inertia is a quantity which is based not just on the mass but the distribution of that mass in the object.
So unless the shape is well defined it is a less useful quantity for performing simple estimates

## Slide 12: Consideration of Torques
We can consider the application of torques in much the same way we did with the linear case
Actuator Torque (τ)
Friction Torque (τ F)
Damping Torque (τ D)
Braking Torque (τ B)
Gravity cause more of a problem in situations like this as for a vertical joint the torque exerted due to gravity will change with angle
It will have no effect on a horizontal plane problem.
τ
τF
τD
τB

## Slide 13: Similar Dynamics Problem
You need your link to move through an angle θ to connect the end effector with a part, it must not exceed the safe angular velocity ω in transit.
Assume link is horizontal and we know the mass of the link and torques involved but we also need to know the length of the link (l) and assume the mass is distributed evenly
Divide the problem into 3 phases
Acceleration phase
(full actuator torque)
Angular velocity(rads/s)
Time (s)
ω
Cruising phase
(actuator torque counters
resistances)
Braking phase
(actuator off, brake on)
τ
τF
τD
τB
Actuator Torque (τ)
Friction Torque (τ F)
Damping Torque (τ D)
Braking Torque (τ B)

## Slide 14: Similar Dynamics Problem
Acceleration Phase.
Assume brake is off, so torque available for angular acceleration is:
τ a = τ - τ F - τ D
So angular acceleration α is: α= τa /I for a rod with centered mass I=ml2/12
Obtain ta from: ω f= ωi+ α t
Obtain θa from: θ = ω it + ½ α t2
Braking Phase.
Assume brake is on, actuator is off so total braking torque is:
τ b = τ B + τ F + τ D
So angular deceleration - α is: α = τ b/I
Obtain tb from: ω f= ω i+ α t
Obtain θ b from: θ = ω it + ½ α t2

## Slide 15: Similar Dynamics Problem
Cruising Phase.
Assume actuator force set to balance resistive forces
τ c = 0
We know the travel angle required is θ and we know the angle travelled in the other two phases. So the angle required in the cruising phase is:
θ c = θ - θ a - θ b
So the joint needs to spend ta with the actuator full on and no brake
tc with the actuator countering resistive torques and
tb with the brake full on and no actuator
At which point it should reach its destination θ at a full stop
So the time in the cruising phase must be tc= θ c / ω

## Slide 16: More Complex Inertia
From this we can get:
  Each particle has mass, dm
  Position of each particle can be obtained using our forward kinematics matrices from yesterday
x
ρ(x)

## Slide 17: More Complex Inertia
To handle more complex moment of inertias we need to consider the link as a set of individual particle each with an inertia.
The density at a position x is r(x),
  usually r is assumed constant
The mass of a link is given by:
The set of material points that comprise the body
The center of mass is:

## Slide 18: More Complex Inertia
Applying our kinematic matrices to the movement of the link we can get an inertial matrix for the link that can be use whatever direction we move in.

## Slide 19: Countering Gravity
Working with torques can also be a good way of estimating actuator strengths to counter the force of gravity.
When a manipulator joint is working against gravity it will be subject to a number of torques generated by the various masses. In effect we need to know:
Each joint must have sufficient actuator torque to counter the moments of the weights on the forward links and joints
weight of each linkage
weight of each joint
weight of object to lift
length of each linkage
L3
End effector
Joint 1
Joint 2
Joint 3
L2
L1
WL1
WJ2
WL2
WJ3
WL3
WEE

## Slide 20: Example
Consider the manipulator below
The robotic manipulator shown below needs to be designed to manipulate a 2kg end effector. Calculate the minimum required motor torques and masses of the structural elements that would be required to hold up the end effector under gravity.
Each joint must have sufficient actuator torque to counter the moments of the weights on the forward links and joints
Motor torque is 1.8 Nm per kg of motor used
Required mass of structural members are 2.5 kg per metre for each kg of mass at end
0.6m
0.8m
0.1m
End effector
Joint 1
Joint 2
Joint 3

## Slide 21: Example
Need to consider the moments generating torque for each joint
Torque on joint due to gravity = sum for each mass of (mass x distance from joint x g)
Mass of structural member 3 from above criteria ML3= 2.5 x ME x L3
= 2.5 x 2 x 0.1 = 0.5 kg
(from holding end effector mass)
L1
End effector
MJ1
gML1
L2
L3
gMJ2
gMJ3
gML2
gML3
gME
Working backwards from the end effector
Torque on Joint 3 = (g x L3/2 x ML3) + (g x L3 x ME)
= (9.81x 0.05 x 0.5) + (9.81x 0.1x 2) = 2.207 Nm
(from moments for end effector and structural member 3)

## Slide 22: Example
So now we can work out the mass of the motorised joint 3
Mass of joint 3 (MJ3) from criteria for joint mass above = 2.207/1.8= 1.226Kg
Mass of structural member 2 from criteria above
ML2= 2.5 x (MJ3 + ML3 +ME) x L2
= 2.5 x (1.226+0.5+2) x 0.8 = 7.452 kg
(from holding joint 3, structural member 3 and end effector mass
Onto Joint 2
Torque on Joint 2
= (g x L2/2 x ML2) + (g x L2 x MJ3) + (g x (L2+ L3/2) x ML3) + (g x (L2 + L3) x ME)
= (9.81x 0.4 x 7.453) + (9.81x 0.8 x 1.226) + (9.81x (0.8+0.05) x 0.5) + (9.81x (0.8+0.1) x 2) =60.69 Nm
(from moments for end effector, structural member 3, joint 3 and structural member 2)
Mass of joint 2 (MJ2) from criteria for joint mass above = 60.69/1.8= 33.72Kg

## Slide 23: Example
Mass of structural member 1 from criteria above
ML1= 2.5 x (MJ2 + ML2 + MJ3 + ML3 +ME) x L1
= 2.5 x (33.72+7.453+1.226+0.5+2) x 0.6 = 66.63 kg
(from holding joint 2, structural member 2, joint 3, structural member 3 and end effector mass)
Finally Joint 1
Torque on Joint 1
= (g x L1/2 x ML1) + (g x L1x Mj2) + (g x (L1 +L2/2) x ML2) + (g x (L1 + L2) x MJ3) + (g x (L1 +L2+ L3/2) x ML3) + (g x (L1+ L2 + L3) x ME)
= (9.81x 0.3 x 66.63) + (9.81x 0.6 x 33.72) + (9.81x (0.6+0.4) x 7.453) + (9.81x (0.6 +0.8) x 1.226) + (9.81x (0.6+0.8+0.05) x 0.5) + (9.81x (0.6+0.8+0.1) x 2)
=514.38Nm
(from moments for end effector, structural member 3, joint 3, structural member 2, joint 2 and structural member 1)
Mass of joint 1 is not required as this is part of the base and does not feature in any calculations

## Slide 24: General Approach
When we are trying to deal with moving masses there are two general approaches used
Newton-Euler approach
  P is absolute linear momentum
  F is resultant external force
  Mo is resultant external moment with respect to point o
  Ho is moment of momentum with respect to point o
Lagrangian (energy methods)
  Kinetic Energy (T)
  Potential Energy (U)
L = K.E. – P.E. = T - U

## Slide 25: Accounting for Gravity Using Lagrange
In the case of a single link rotating with the effects of gravity it is possible to derive a time varying equation for the torque.
2
 ;
T 
m(  ) 
U  mg( a  a cos )
2 2
1 a ˙ 1 ma2
2 2 2 12
˙2
dt
3  2
d ( L )  1 ma 2  ; L   1 mga sin
˙
1 ma2˙  1 mga sin  
3 2
a
2
6
ma2
(1 cos )
  mg
L  T -U 
˙2
Kinetic Energy
Potential Energy
Total Energy
.

## Slide 26: Other Forces
When your dynamic problem goes beyond a single link other forces come into play.
Centripetal Force
Coriolis Force
Centripetal Force is due to the effect on link 2 of being spun by link 1
Coriolis Force is due link 2 moving in the rotating reference frame of link 1

## Slide 27: Multi Link Dynamics
For a multi link manipulator we must use matrix transformations again like the ones you saw in the kinematic lectures.
The Acceleration-related Inertia matrix term
The Coriolis and Centrifugal terms
The Gravity terms
Driving torque applied on each link
Joint accelerations
Static form (gravity only)

## Slide 28: Puma 560
Example of calculation required for a PUMA 560

## Slide 29
Example of calculation required for a PUMA 560
D, H, C terms

## Slide 30
Example of calculation required for a PUMA 560
D, H, C terms

## Slide 31
Example of calculation required for a PUMA 560
D, H, C terms

## Slide 32
Example of calculation required for a PUMA 560
D, H, C terms

## Slide 33: Reality
Even the matrix derived dynamics still requires accurate description of the moment of inertia for the given link
Most robot part are tested empirically to determine their characteristic first in order to simplify that application of a dynamic model